## Slide 1
1
1

## Slide 2
LOGICAL GATE
LOGICAL GATE ARE ELECTRONIC COMPONENTS THE OUTPUT OF GATE BASED ON ONE OR MORE INPUTS
TWO VOLTAGE LEVELS CAN BE REPRESENTED AS THE TWO DIGITS 0 AND 1

## Slide 3
ORDERED LOGIC GATES (SIMPLE EXPLANATION)
AND GATE → OUTPUTS 1 ONLY IF BOTH INPUTS ARE 1.
NAND GATE → OPPOSITE OF AND, OUTPUTS 0 ONLY IF BOTH INPUTS ARE 1.
OR GATE → OUTPUTS 1 IF AT LEAST ONE INPUT IS 1.
NOR GATE → OPPOSITE OF OR, OUTPUTS 1 ONLY IF BOTH INPUTS ARE 0.
XOR GATE → OUTPUTS 1 IF INPUTS ARE DIFFERENT.
XNOR GATE → OUTPUTS 1 IF INPUTS ARE THE SAME.
BUFFER → PASSES THE INPUT UNCHANGED (0 → 0, 1 → 1).

## Slide 15
Arithmetic Operations
These operations perform mathematical calculations.
  Addition (ADD)
  Subtraction (SUB)
  Multiplication (MUL)
  Division (DIV)
  Increment (INC) & Decrement (DEC)
Types of Operation
Data Transfer Operations
These operations move data between memory, registers, and input/output devices.
  Load (LD) – Move data from memory to a register.
  Store (ST) – Move data from a register to memory.
  Move (MOV) – Transfer data between registers.
  Push & Pop – Stack operations for saving/restoring values.

## Slide 16
Logical Operations
These operations perform bitwise logic on binary values.
  AND – Bitwise AND operation.
  OR – Bitwise OR operation.
  XOR – Bitwise XOR (exclusive OR).
  NOT – Bitwise negation.
  Shift (SHL, SHR) – Left and right shift operations.
Control Operations (Branching & Jumping)
These operations change the flow of execution in a program.
  Jump (JMP) – Unconditional jump to another instruction.
  Branch (BEQ, BNE, etc.) – Conditional jumps based on comparison results.
  Call & Return (CALL, RET) – Used for function calls.
  Looping Instructions – Iterative execution of instructions

## Slide 17
Comparison Operations
These operations compare values and set flags for decision-making.
  Compare (CMP) – Compares two values.
  Test (TEST) – Similar to CMP but for logical conditions.
Bit Manipulation Operations
These are used for modifying specific bits in a word.
  Set, Clear, Toggle Bits (SET, CLR, TGL)
  Rotate (ROL, ROR)
Input/Output Operations
These operations manage data exchange with external devices.
  IN – Read data from an input port.
  OUT – Send data to an output port.

## Slide 18
System Control Operations
These are privileged operations that control system behavior.
  HALT (HLT) – Stops the CPU.
  NOP (No Operation) – Does nothing but advances the instruction pointer.
  Interrupt (INT) – Handles system calls or hardware interrupts.

## Slide 19
Types of Bus in Computer Architecture
  Data Bus – Transfers actual data between CPU, memory, and I/O devices (bi-directional).
  Address Bus – Carries memory addresses from CPU to memory/I/O (uni-directional).
  Control Bus – Sends control signals for coordinating operations (read, write, interrupts).
  System Bus – A combination of data, address, and control buses for internal communication.
  I/O Bus – Connects external devices like USB, PCIe, and SATA.
  Memory Bus – High-speed link between CPU and RAM for fast memory access.
  Parallel Bus – Transfers multiple bits simultaneously for short distances.

## Slide 20
Intro to Registers

## Slide 23
Basic general purpose registers
  EAX
  EBX
  ECX
  EDX

## Slide 24
Internal structure of each register (32-bit)
EAX is dword which is 4 bytes (32 bits)
AX is a word which is 2 bytes (16 bits)
AH is a byte (8 bits)
AL is also a byte (8 bits)
If EAX = 0x12345678
AX = 5678
AH = 56
AL = 78

## Slide 25
Same for EBX, ECX, EDX
For EBX,
If EBX = 0x12345678
BX = 5678
BH = 56
BL = 78

## Slide 27
64-bit registers
RAX is qword which is 8 bytes (64 bits)
EAX is a dword which is 4 bytes (32 bits)
AX is word which is 2 bytes (16 bits)
AH is a byte (8 bits)
AL is also a byte (8 bits)

## Slide 28
ESI, EDI, EIP, ESP, EBP registers
String index registers:
ESI = Source Index
EDI = Destination Index
Instruction pointer:
EIP indicates the memory current address of current instruction
Stack Frame Pointers:
ESP = address of top of stack
EBP = address of bottom of stack

## Slide 30
next

## Slide 31
MOV Instructions

## Slide 32
  MOV Destination, Source
  Copies data from Source to Destination
  Example:
    mov eax, 0x3A
    mov al, 0x8
    mov ebx, eax
    mov cx, bx
    mov ah, cl

## Slide 33
Basic Arithmetic

## Slide 34
Examples
  ADD destination, source
  Destination  destination + source
  add eax, ecx
  add edi, 0x2A
  add cx, si

## Slide 35
Dword registers
  mov esi, 0x1
  mov eax, 0x2
  mov ebx, 0x3
  add eax, ebx
  add eax, eax
  mov esi, 0xFFFFFFFF
  add ebx, esi
  add esi, eax

## Slide 36
Partial Registers
  mov edi, 0xAB29FFFF
  mov ecx, 0x00000703
  mov eax, 0x000000FF
  add al, ch
  add di, cx
  mov edi, 0xAB29FFFF
  add edi, ecx

## Slide 37
Basic Arithmetic
SUB Instruction

## Slide 38
Examples
  SUB destination, source
  destination  destination - source
  sub eax, edx
  sub edi, 0x2A
  sub cl, dl

## Slide 39
INC and DEC
Instructions

## Slide 40
Examples of INC
  INC register
  register  register + 1
  inc eax
  eax  eax + 1

## Slide 41
Examples of DEC
  DEC register
  register  register - 1
  dec si
  si si - 1

## Slide 42
MUL (Multiply)
Instructions

## Slide 43
Examples of MUL
  MUL register
  ax  al . register
  dx:ax  ax . register
  edx:eax  eax . register
  edx:eax means that edx and eax are concatenated together
  Note that the size of the result is twice the size of the argument

## Slide 44
Intro to JUMPS

## Slide 45
Two types of JUMPS
  Un-conditional jumps
  jmp 0x04012428
  Conditional jumps
  jz 0x04012428
  jnz 0x04012428

## Slide 46
Conditional JUMPS
  Based on values inside flags register

## Slide 47
JZ (Jump Zero)
  jumps only if the ZF is set to 1 (i.e. the result of the last calculation is zero), eg:
  mov eax, 0x1
  dec eax
  jz 0x04012428
  add eax, 0x5
  0x04012428 add eax, 0x2
  Jump is taken
  EAX = 2

## Slide 48
JNZ (Jump Not Zero)
  jumps only if the ZF is cleared to 0 (i.e. the result of the last calculation is non-zero), eg:
  mov eax, 0x1
  inc eax
  jnz 0x04012428
  add eax, 0x5
  0x04012428 add eax, 0x2
  Jump is taken
  EAX = 4

## Slide 49
Other jumps

## Slide 50
JS and JNS
  JS = Jump if SF (sign flag) is set
  JNS = Jump if SF is cleared

## Slide 51
JC and JNC
  JC = Jump if CF (carry flag) is set
  JNC = Jump if CF is cleared

## Slide 52
JO and JNO
  JO = Jump if OF (overflow flag) is set
  JNO = Jump if OF is cleared

## Slide 53
Reading Flags Register Indirectly
  Cannot read Flags Register directly
  So, we can use the conditional jumps as an indirect way to read the Flags Register

## Slide 54
Intro to CMP instructions

## Slide 55
CMP (compare instruction)
  CMP is used to compare 2 numbers
  CMP A, B
  A – B, then changes flags accordingly but does not change A or B
  JC is also known as JB (Jump if Below)

## Slide 56
Comparing unsigned and signed numbers

## Slide 57
CMP unsigned numbers
  The following instructions are for unsigned comparisons:
  JB = Jump if Below
  JBE = Jump if Below or Equal
  JA = Jump if Above
  JAE = Jump if Above or Equal

## Slide 58
Jump Instruction | Intuitive Meaning
JB (Jump Below) | Jump if EAX is Below EBX (EAX < EBX)
JBE (Jump Below or Equal) | Jump if EAX is Below EBX, or, Equal (EAX <= EBX)
JA (Jump Above) | Jump if EAX is Above EBX (EAX > EBX)
JAE (Jump Above or Equal) | Jump if EAX is Above EBX, or, Equal (EAX >= EBX)
CMP unsigned numbers (3)
JB is the same as JC (Jump Carry)
JAE is the same as JNC (Jump if No Carry)
An intuitive way to understand the Jump Instructions:
Assuming: CMP EAX, EBX

## Slide 59
CMP signed numbers
  The following instructions are for signed comparisons:
  JL = Jump if Less
  JLE = Jump if Less or Equal
  JG = Jump if Greater
  JGE = Jump if Greater or Equal